## Slide 1: Bed Occupancy Alarm clock
Getting you out of bed since 2020
(kicked you in the behind and left you on the curb wearing pajamas)
Dana Deutsch

## Slide 2: If you fall back to sleep after turning off your alarm, or don’t have the motivation to leave the bed, this product is for you

## Slide 3: The alarm that knows if you left the bed
Senses when your phone alarm goes off
Short snooze which cant be completely turned off until you leave the bed
Keeps checking bed status until an hour after you get out of bed before stopping the cycle

## Slide 4: Components –Sensors and Actuators
Buzzer and Microphone sensor Under here
Push Button
MSP430 and HX711 Amplifier and ADC Board
Two 50kg Half Bridges Load Sensors

## Slide 5: Components - Display
Previous Sleep Cycle Info
Real time ADC Value Plot
Current Cycle Info
1. Real Time Entered Bed of Bed Entry Before Alarm
2. Amount of Time Slept Before Alarm
3. How Long It took to Get Up and Stay Up
Connection Info
For Graph

## Slide 7: Thank You For Watching

## Slide 8: Flow diagram

## Slide 9: System Components Summery
MSP430
Half Bridge Load Sensors
Amplifier and ADC for Wheatstone Bridge circuit strain gauge signal conditioning
Push Button
Piezo Buzzer
Microphone Sensor
Optional: C# Information Display on laptop

## Slide 10: Shortened Example Cycle
Enter Bed
Phone Alarm
47
Amount Slept
Enter bed and go to sleep – Woken Up by phone alarm – Turn off but stay in Bed
We see spikes because I lean on the corner/edge of the bed where the sensor is located when reaching to turn off the alarms

## Slide 11: Shortened Example Cycle
Exit Bed
Buzzers
60
Amount To Wake up
Buzzers
Buzzers
15
15
15
We see spikes because I lean on the corner/edge of the bed where the sensor is located when reaching to turn off the alarms
Snooze rings every 15 seconds after turning off the phone alarm until we leave the bed

## Slide 12: Shortened Example Cycle
124
New Time To Wake up
Buzzers
15
15
29
We see spikes because I lean on the corner/edge of the bed where the sensor is located when reaching to turn off the alarms
Returning under 2 min will keep reinitializing the snooze cycles

## Slide 13: Shortened Example Cycle
188
44
We see spikes because I lean on the corner/edge of the bed where the sensor is located when reaching to turn off the alarms
After 2min system cycle ends bed can be entered safely
In bed with no Buzzer

## Slide 14: Bed Occupancy Alarm Clock System
Snooze